## Slide 1: Strain Limiting and Position Based Dynamics

## Slide 2: The Stiffness Issue
Real-world fabrics resist strongly to stretching, once they stretch beyond certain limits.
But, increasing the stiffness can cause problems.
  Explicit integrators will be unstable
    Solution: smaller time steps and more computational time.
  The linear systems involved in Implicit integrators will be ill-conditioned.
    Solution: more iterations and computational time.
Can we achieve high stiffness, with a low computational cost?

## Slide 3: A Single Spring
If a spring is infinitely stiff, we can treat the length as a constraint and define a projection function.
rest length
Constraint
Stretched case
Compressed Case

## Slide 4: A Single Spring
If a spring is infinitely stiff, we can treat the length as a constraint and define a projection function.
rest length
Constraint
such that
Boundary

## Slide 5: A Single Spring
If a spring is infinitely stiff, we can treat the length as a constraint and define a projection function.
rest length
Constraint
such that
By default, , but we can also set for stationary nodes.

## Slide 6: Multiple Springs – A Gauss-Seidel Approach
What about multiple springs? The Gauss-Seidel approach projects each spring sequentially in a certain order. Imagine two springs with unit rest lengths…
2
2
1
2.5
1.75
1
1.375
1
1
1.1875

## Slide 7: Multiple Springs – A Gauss-Seidel Approach
We cannot ensure the satisfaction of every constraint. But the more iterations we use, the better those constraints are satisfied.
Although the name is related to Gauss-Seidel, it differs from Gauss-Seidel. It is more relevant to stochastic gradient descent (in machine learning).
The order matters. The order can cause bias and affect convergence behavior.
For every edge
For
Projection (by Gauss-Seidel)

## Slide 8: Multiple Springs – A Jacobi Approach
To avoid bias, the Jacobi approach projects all of the edges simultaneously and then linearly blend the results.
The problem is an even lower convergence rate.
Again, the more iterations it uses, the better the constraints are enforced.
For every edge
For
For every vertex
For every vertex
Projection (by Jacobi)

## Slide 9: Position Based Dynamics (PBD)
Position based dynamics (PBD) is based on the projection function.
A PBD Simulator
//Do Simulation, update and
//Now PBD starts.
The stiffness behavior, i.e., how tightly constraints are enforced, is subject to non-physical factors.
  The number of iterations
  The mesh resolution
The velocity update following projection is important to dynamic effects.
This method is applicable to other constraints as well, including triangle constraints, volume constraints, and collision constraints.
  To implement these constraints, simply define their projection functions.

## Slide 10: Pros and Cons of PBD
Pros
  Parallelable on GPUs (PhysX)
  Easy to implement
  Fast in low resolutions
  Generic, can handle other coupling and constraints, including fluids
Cons
  Not physically correct
  Low performance in high resolutions
    Hierarchical approaches (can cause oscillation and other issues…)
    Acceleration approaches, like Chebyshev

## Slide 11: After-Class Reading
Muller. 2008. Hierarchical Position Based Dynamics. VRIPHYS.